## Slide 1: Lecture 7 CAD Connections

## Slide 2: CAD Connections
What will you learn from this presentation:
  Geometry Import Properties
  CAD Connections
  Uni/Bi-Directional Connectivity
  Named Selection Manager

## Slide 3: Preprocessing Workflow
Sketches and Planes
Geometry Import Options
3D Operations
Direct CAD/Bi-Directional CAD
Geometry Cleanup and Repair
Automatic Cleanup
Merge, Connect, Projection, Flow Volume Extraction, etc
Extrude, Revolve, Sweep, etc
3D Operations
Boolean, Body Operations, Split, etc
Geometry Creation
OR
Geometry Import
Meshing
Solver
Geometry Operations
Meshing Methods
Hybrid Mesh: Tet, Prisms, Pyramids
Hexa Dominant, Sweep meshing
Global Mesh Settings
Local Mesh Settings
Sizing, Body/Sphere of Influence, Match Control, etc
Assembly Meshing

## Slide 4: Geometry Properties (1)
Geometry Properties are import and data transfer related properties which will be applicable for imports
Right click on Geometry cell on Project Schematics and select Properties
Most of the settings for import can be done through “Basic Geometry Options” and “Advanced Geometry Options”
Several things can be setup as default such as
  Default analysis type (3d/2d)
  Import/export options
    Parameters
    Named Selections, etc.

## Slide 5: Geometry Properties (2)
Basic Properties :
Select ‘Parameters’ option for importing parameters defined in CAD package
‘Parameter Key’ filters the parameters from CAD that enter Workbench
If ‘Parameter Key’ is not specified, all parameters from CAD enter Workbench
Similarly, Named Selections key controls the selections from CAD entering WB

## Slide 6: Geometry Properties (3)
Advanced Properties :
Select ‘Use Associativity’ to establish association between CAD and WorkBench
Import Coordinate Systems, Work Points, etc. defined in CAD
Smart CAD Update :
    If selected, changes made in other options get updated in the model

## Slide 7: CAD Connections: Introduction
CAD Connections
  Transfer CAD geometry to DesignModeler/Meshing
  Two approaches
    Approach I (Import)
      Import neutral/native CAD files directly into DesignModeler
      Uni-directional connectivity
    Approach II (Direct Connection)
      Use Plug-In (Associative Interface)
      Bi-directional CAD Connectivity
      ANSYS Direct CAD Interface
  Pro/ENGINEER
  DM

## Slide 8: CAD Connections: Supported Readers & Plug-Ins/Interfaces
Reader Version
  ACIS (*.sat, *.sab) 22
  ANSYS BladeGen (.bgd) 12
  Catia V4 (*.model,*.exp,*.session,*.dlv) 4.2.4
  Catia V5 (*.CATPart, *.CATProduct) V5-6R 2012
  Catia V5 CADNexus CAPRI CAE V5R 20, R21
  Catia V5 CADNexus CAPRI CAE V5R 19
  Creo Parametric (*.prt, *.asm) 1.0
  Gambit (*.dbs) 2.4
  IGES (*.igs, *.iges) 4.0, 5.2, 5.3
  Autodesk Inventor (*.ipt, *.iam) 2012
  JT Open (*.jt) 8.0, 8.1
  Monte Carlo N-Particle (*.mcnp)
  NX (*.prt) 8.0
  Parasolid (*.x_t/b, *.xmt_txt/bin) 24.1
  SolidWorks (*.sldprt, *.sldasm) 2012
  Step (*.stp, *.step) AP203, AP214
Reader/Plug-In/Interface Version
  Autodesk AutoCAD (*.dwg, *.dxf) 2012, 2013
  Creo E/Direct Modeling (*.pkg,*.bdl,*.ses,*.sda,*.sdp,*.sdac,*.sdpc)
  17.0, 18.0, 18.1
  Creo P (Pro/Engineer) (*.prt, *.asm) Creo Parametric 1.0, 2.0
  Wildfire 5.0
  Autodesk Inventor (*.ipt, *.iam) 2012, 2013
  NX (*.prt) 6.0, 7.5, 8.0
  Solid Edge (*.par,*.asm,*.psm,*.pwd) ST3, ST4
  SolidWorks (*.sldprt, *.sldasm) 2011, 2012
  TeamCenter (Plug-In) Unified 8.1 with NX 7.5 Unified 8.3 with NX 7.5.2 Engineering 9.1 with NX 8.0
  SpaceClaim (SCDM) (*.scdoc) 2012 SP1
  For Full Platform/OS Specific Support Consult Documentation (CAD Integration)

## Slide 9: CAD Connections: Approach I
Three ways to import file in WB
  Import option on Workbench project page (File  Import)
  Geometry cell on project page
    Right click for Context Menu
  Import in existing DM session
    Appends the geometry file to existing geometry in DM
    Multiple imports possible

## Slide 10: CAD Connections: Approach II
Launch Workbench from CAD system
  Bi-Directional CAD Connectivity
    Export parameters from CAD to Workbench
    Parameter change in CAD reflects in Workbench and vice versa
  Bidirectional import from DM session
    Attach to Active CAD Geometry
    Imports active CAD geometry in DM
    Can attach only saved CAD sessions
  Parameter Key
    Prefix key for importing parameters
    Default filter set to DS. Remove to import all parameters
  Direct CAD Connection in UG NX
  Parameter Check Box & Key
  Attach option in DM

## Slide 11: CAD Connections: Bi-Directional CAD
Pro/ENGINEER
DesignModeler
Parameterized Hole Dia and No of Holes
Parameters from CAD to Workbench
Parameters from Workbench to CAD

## Slide 12: CAD Connections: Named Selection Manager
Named Selections
  Define in CAD & transfer to WB
  Define directly under WB
  Named Selection filter under WB
    By default the filter is set to NS
    Available if the “Import Named Selections” option is set to Yes
    Default filter set to NS. Remove to import all parameters
  Named Selection Manager in UG NX
  Workbench Geometry Import Options

## Slide 13: CAD Connections: Named Selection Manager
  Named Selection defined in UG NX
  Named Selection imported in WB

## Slide 14: Pre-requisites for CAD Connections
  For all CAD packages
    CAD correctly installed and licensed
    Correct ANSYS Inc. license
  For CATIA
    Compatible version of CATIA V5 CAD program (R17, R18, R19, R20 or R21).
    IBM LUM 4.6.8 or DSLS configured with a CATIA V5 (MD2, HD2, or ME2) license.
    CADNexus CAPRI Gateway V3.15.2.
  For UG NX
    All NX bodies must be within a 1000 x 1000 x 1000 meter cube, centered about the origin of the absolute coordinate system.
  For UG NX
    Some solids, surfaces and lines containing Bspline geometries may not import correctly into the DesignModeler application, but should import correctly in the ANSYS Mechanical application.
    NX 5.0.6 or higher is recommended for importing models containing spot welds
    After installation of ANSYS Workbench, importing an NX model using the Reader mode requires the CAD be launched one time.
  Refer to the documentation for further details on licensing requirements

## Slide 15: CAD Connections: Advanced Geometry Options
  Analysis Type
    Specify 2D or 3D simulation
  Use Associativity
    To allow CAD associativity
  Import Coordinate Systems
    Import CAD coordinate system
  Import Work Points
    Import work points defined in CAD
  Reader Mode Saves Updated File
    Save CAD file at the end of update
  Import Using Instances
    Import part instances from CAD
  Smart CAD Update
    Accelerate refresh of modified parts
  Enclosure and Symmetry Processing
    Automatically creates named selections if turned ON
  Mixed Import Resolution
    Import parts with mixed dimensions

## Slide 16: Gambit Reader
Importing Legacy Gambit Models
  This is a stand-alone reader that does not require an installation of the GAMBIT program or GAMBIT licenses.
    Supports real and virtual geometry import.
    No CAD associativity.
    No CAD Parameters.
    Supports GAMBIT volumes, faces, edges, and vertices (excluding stand-alone vertices).Reads Real (ACIS) geometry from a Gambit database
    Does not include reading meshing information