## Slide 1: Lecture 10 Lines and Surfaces (Concept Modeling)

## Slide 2: Introduction
Why is Concept Modeling relevant for CFD users?
Sometimes the imported files contain issues like:
    Missing Faces
    Corrupt Faces
    Details which require cleanup by selective geometry recreation
  For cleaning, patching, recreating surfaces & stitching a water tight body, several line and surface creation options of concept modeling are used
  CFD models also require some solids/thin bodies to be modeled as zero thickness surfaces
    Examples are baffles, fins, zero thickness pipe walls, fan shrouds, etc.
  For above mentioned cases mid-surfacing tools need to be used
  Sometimes 2D modeling operations also require use of concept modeling tools

## Slide 3: Lines and Surfaces
  The features in the Concept menu are predominantly used to create and modify line bodies and/or surface bodies
  For modeling lines and surfaces, you can also:
    Create line or surface bodies using the features in the Draw toolbox to design a 2D sketch and/or generate a 3D model
    Use the Import external geometry file feature
    Mid-surfaces can be used for converting a body into zero thickness surface (e.g. Fins, Baffles, Fan shroud, etc.)
    Other tools like Thin, Extrude, etc.
  Line bodies
    Lines from points
    Lines from sketches
    Lines from edges
  Surface bodies
    Surfaces from line bodies
    Surfaces from sketches
    Surfaces from 3D edges
    Mid-surface
    Joint

## Slide 4: Creating Line Bodies (1)
Lines From Points
[Main Menu] Concept  Lines From Points
    Points can be any 2D sketch points, 3D model vertices or Point Feature (PF) points.
    A point segment is a straight line connecting two selected points.
    The feature can produce multiple Line Bodies, depending on the connectivity of the chosen point segments.
    The Operation field allows Add or Add Frozen choices for line bodies.
Point 1
Point 2
Line Body

## Slide 5: Creating Line Bodies (2)
Lines From Sketches
[Main Menu] Concept  Lines From Sketches
    Line bodies created based on sketches and planes from faces
    Multiple Line Bodies may be created depending on the connectivity of the edges within the base objects
    Select sketches or planes in the feature tree then “Apply” in the detail window
    Multiple sketches, planes, and combinations of sketches and planes can be used as the base object for the creation of line bodies

## Slide 6: Creating Line Bodies (3)
Lines From Edges
[Main Menu] Concept  Lines From Edges
    Creates line bodies based on existing 2D and 3D model edges
    Can produce multiple line bodies depending on the connectivity of the selected edges and faces
    Can select edges and/or faces through two fields in the detail window then “Apply”
Line Bodies

## Slide 7: Split Edges
Split Line Body
[Main Menu] Concept  Split Edges
    Splits line body edges into two pieces
    Split location is controlled by the Fraction property (e.g. 0.5 = split in half).
    Other Options:
      Split by Delta: Distance between each split is given by Delta along the edge
      Split by N: Number of Divisions of the Edge
Selected line
Fraction = 0.5
Fraction = 0.25

## Slide 8: Cross Sections (1)
Cross Sections
    Cross sections are attributes assigned to line bodies to define beam properties in the FE simulation
    In DM, cross sections are represented by sketches and are controlled by a set of dimensions
      Note: Design-Modeler uses a different coordinate system for cross sections than the one used in the ANSYS environment (described later)

## Slide 9: Cross Sections (2)
Cross sections are selected from the Concept menu
A cross section branch is inserted in the tree where each chosen cross section is listed
Cross Sections in Tree Outline
Concept Menu
List of Cross Sections

## Slide 10: Cross Sections (3)
Assigning a cross section to a line body:
    Highlight the line body in the Tree
    A cross section property appears in the detail window
    Click in this field and choose the desired cross section from the drop down list

## Slide 11: Surfaces From Edges (1)
Surfaces From Edges
[Main Menu] Concept  Surfaces from Edges
    Creates surface body using line body edges as the boundary
    Line body edges must form non-intersecting closed loops
    Each closed loop creates a frozen Surface Body
    The loops should form a shape such that a simple surface can be inserted into the model:
      Planes, cylinders, tori, cones, spheres and simple twisted surfaces
Planar surface
Non-planar surface
Details window:
  Flip surface normals
  Input thickness which will be transferred to the FE model

## Slide 12: Surfaces From Edges (2)
Creates surfaces from existing body edges
Can be solid or line body edges
Edges must produce non-intersecting closed loops
Existing solid body edges are selected for new surface boundary.
New, frozen, surface body generated (note, solid body is hidden).

## Slide 13: Surfaces From Edges (3)
  A line body with no cross section can be used to tie together surface models
  In this case, the line body acts merely as a mechanism to insure a continuous mesh at the surface boundaries
Line Body (no cross section)
Result is continuous FE mesh at surface interface
2 Surface Bodies

## Slide 14: Surfaces From Sketches
Surfaces From Sketches
[Main Menu] Concept  Surfaces from Sketches
        Creates surface bodies using sketches as boundaries (single or multiple sketches are OK)
        Base sketches must be closed profiles which are not self intersecting
        May choose to “Add” or “Add Frozen” operations
        Can reverse normal direction “No” in Orient With Plane Normal field
        Can enter thickness which will be used in creating the FE model

## Slide 15: Mid-Surface
Extracts surface body that is midway between existing solid body faces
Two Options:
    Manual: Operates only on user specified face pairs
    Automatic: Provides option to search for other matching face pairs
  Details View of Mid-Surface
  Mid-Surface created for a pipe geometry

## Slide 16: Mid-Surface: Manual (1)
  Manual Method
  Set the Selection Method to “Manual”
  Select pair of faces, one pair at a time, in Face Pairs input
  The order of selection determines the surface normal direction
  Notice the first surface picked is displayed in purple, the second is shown in pink
  When the selection is finalized the selected pairs are displayed in dark and light blue colors
  Details View of Mid-Surface
2nd Pick
1st Pick
Normal Direction
  Solid Model
  Color of faces during selection
  Color of faces after selection

## Slide 17: Mid-Surface: Manual (2)
  Multiple surface pairs may be selected for a single mid-surface operation, however they must be selected as opposing pairs
  The correct order of selection of faces for the previous example can be as in the image shown on right hand side here
  Adjacent face pairs will be grouped together if within the “Thickness Tolerance” (see below)
  Order of face selection
3
1
5
4
6
2
T1
T2
If │T1 – T2│ < Thickness Tolerance: surfaces are grouped

## Slide 18: Mid-Surface: Automatic (1)
Automatic Method
  Switching the Selection Method from “Manual” to “Automatic” exposes several additional options
    Bodies to search: Limits search to visible bodies, selected bodies or all bodies
    Minimum and maximum threshold sets search range (thickness) for face pairs
  Options like Extra Trimming are very useful with “Automatic” method
    Provides options for situations where trimming problems with surface bodies occur
  Preserve Bodies? allows you to save the solid bodies from which surfaces are created (default is No)

## Slide 19
  When the search is complete, the number of pairs detected is listed in the details and displayed graphically
  Mid surface creation is completed by Generating the surface body
Mid-Surface: Automatic (2)

## Slide 20: Joint
Joins surface bodies together such that their contact regions share common edge
    Prerequisite for conformal meshes
Takes two or more surface bodies as input
Imprints edges on all bodies where they make contact
  Details View of Joint
  Surface bodies to be Joined
  Surface bodies after Joint

## Slide 21: Edge Joints (1)
Edge Joints are the glue that holds together bodies where a continuous mesh is desired
Creating surface and/or line multi-body parts with coincident edges results in automatic creation of edge joints
Joints can be created manually ([Main Menu] Tools  Joint) where no coincident topology exists

## Slide 22: Edge Joints (2)
Edge Joints can be viewed by turning on the Edge Joints option in the View menu.
Edge joints are displayed in either blue or red.
    Blue: edge joint is contained in properly defined multi-body part
    Red: edge joint not grouped into the same part
No Edge Joint
With Edge Joint