## Slide 1: Workshop 5a Applications – Mixing Tank

## Slide 2: Introduction
Background
  This workshop will demonstrate the practical application of ANSYS Meshing to a mixing tank model. Access to DesignModeler is required.
Objectives
  Starting ANSYS Meshing
  Generating a mesh
  Decomposing for Sweep Meshing
  Local Sizing
  Using Advanced Size Functions
  Using Inflation
  Named Selections

## Slide 3: Project Startup
Create the Project
  Start Workbench.
    Start  All Programs  ANSYS 14.5  Workbench 14.5
    This workshop uses the geometry created in workshop 5a of the DesignModeler course. Open your saved project (DMWS5a) and drag and drop a Meshing component system onto the Geometry Cell (A2) as shown.
    If you did not complete this workshop, a copy is provided in the Meshing Workshops Input-Files folder.
    Double click on the Mesh Cell B3 to start Meshing.

## Slide 4: Units
Set Units
  From the main menu select Units and, if it is not already set, specify Metric (m...).

## Slide 5: Geometry
View the Geometry
  Expand the Geometry Object in the Outline and select both bodies (CTRL click to multiple select).
  In the Details View, under Graphics Properties set Transparency to 0.5.
  Click the Mesh Object in the Outline.

## Slide 6: Preparation
Planning
  This geometry contains two single body parts, an inner body containing the rotating impeller and, a stationary outer body. This will result in a non-conformal interface which will allow the impeller to rotate in the simulation.
  The impeller body is complex and so the Tetrahedrons Method combined with Advanced Size Functions to capture curvature would be a good candidate.
  Inflation will also be used on the impeller surfaces to capture boundary layer gradients.
  The same method could be applied to the outer body for simplicity. However, some simple slicing operations in DesignModeler will allow more efficient sweep methods to be applied.

## Slide 7: Global Mesh Settings
Mesh
  In Details of “Mesh”, set the following under Defaults;
    Physics Preference: CFD.
    Solver Preference: FLUENT.
  Under Sizing, set;
    Use Advanced Size Function: On: Curvature.
    Relevance Center: Fine.
  Leave all other settings to Default.
    We will apply inflation later.

## Slide 8: Initial Mesh
Generate Mesh
  Generate the Mesh.
  Snap to the +Z view using the Axis Triad.
  Select the Section Plane button’
  Create a section by clicking , dragging down and releasing to define a vertical slice as shown.
  Snap to the Iso View.

## Slide 9: Initial Mesh
View the Mesh Interior
  Zoom into the impeller body as shown using the Box Zoom Tool.
  The Automatic Method has applied Patch Conforming Tetrahedrons refining for curvature where required.
  The Non-Conformal Interface between the impeller and the outer body is clearly visible. Switch off the Slice Plane.
  To gain the advantages of a hex sweep mesh we’ll need to make some simple but important modifications to the geometry.

## Slide 10: Preparation
Planning
  To enable the application of sweep hex mesh methods the geometry will be decomposed in DesignModeler.
  Two slice operations will be performed.
    The first will use the impeller body side faces to slice vertically through the outer body.
    The second will slice through using the XYPlane.
  This will leave four outer annular bodies (two shown here for clarity) which can be swept meshed radially around the axis and one lower cylindrical body which can be swept meshed upwards.
  The impeller body will be left in its existing form and meshed with Tetrahedrons.
Sweep Up
Sweep Round
Tetrahedrons

## Slide 11: Decomposition in DesignModeler
Open DesignModeler
  From the Workbench Project Schematic, double click the Geometry Cell (A2) to launch DesignModeler.
    Do not close the Meshing Application.

## Slide 12: Decomposition in DesignModeler
Slice 1
  In DesignModeler, select Slice from the Create Menu.
  In the Details View set Slice Type to Slice by Surface.
  Activate the Target Face Selection Box .
  Select the face dividing the impeller body from the outer body by clicking on it and selecting the appropriate selection pane in the lower left corner of the Graphics Window. Apply the Selection.
  Set Slice Targets to All Bodies.
  Generate.

## Slide 13: Decomposition in DesignModeler
Slice 2
  Select Slice again from the Create Menu.
  In the Details View set Slice Type to Slice by Plane.
  Activate the Base Plane Selection Box .
  Select the XYPlane from the Tree Outline and apply the Selection.
  Set Slice Targets to Selected Bodies and select the two bodies as shown.
  Apply the selection and Generate.
1
2

## Slide 14: Decomposition in DesignModeler
Form a Multi-Body Part
  We need the five new outer bodies to be conformal. Select the five as shown, right click and select Form New Part from the Context Menu.
1
2
3
4
5

## Slide 15: Decomposition in DesignModeler
Review
  Check you have 2 Parts, 6 Bodies as shown.
  Close DesignModeler and return to the Meshing Application.

## Slide 16: Refresh Geometry
Attach the New Geometry
  In the Meshing Application, from the Outline, right click on Geometry and select Update Geometry from Source.
  When the modified geometry has loaded generate the mesh using the existing settings.
  Select the Mesh Object in the Outline to view the new mesh.

## Slide 17: Sweep Mesh
View the Mesh
  The Meshing Application has now automatically applied Sweep Methods to the new sweepable bodies.
  Switch on the Section Plane to study the mesh interior.
  Switch off the Section Plane when ready to proceed.

## Slide 18: Preparation
Planning
  To better control the sweep mesh we’ll apply some local edge sizing controls.
  We’ll specify a fixed number of divisions to control the sweep around the axis.
  To control the sizing of the mesh radially we’ll apply biased edge sizing to ensure the cell size decreases nearer to the centre.
Biased Sizing
Fixed Number of Divisions

## Slide 19: Local Sizing
Add Edge Sizing
  Right click on the Mesh Object in the Outline and select Clear Generated Data from the Context Menu to clear the mesh. Answer Yes.
  Select the Edge Selection Filter.
  Select the four edges as shown (CTRL click for multiple select).
  Right click in the Graphics Window and select Insert  Sizing from the context Menu.

## Slide 20: Local Sizing
Add Edge Sizing
  Under Details of “Edge Sizing” set;
    Type: Number of Divisions.
    Number of Divisions: 40.
    Behavior: Hard.
  The specified Edge Sizing will be previewed on the geometry.

## Slide 21: Local Sizing
Add Biased Edge Sizing
  Ensure the view is set to isometric.
  Select the body as shown, right click and select Hide All Other Bodies from the Context Menu.

## Slide 22: Local Sizing
Add Edge Sizing
  Select the Display Edge Direction button.
  The direction sense shown on the edges will dictate the direction of any applied biasing.
  If the direction of all four edges were pointing towards or away from the centre we could apply one biased sizing, since they are not we must apply two.
  Switch off the Display Edge Sense by clicking the button again.

## Slide 23: Local Sizing
Add Biased Edge Sizing
  Select the two edges as shown, right click Insert  Sizing.
  Under Details of “Edge Sizing” set;
    Type: Number of Divisions.
    Number of Divisions: 30.
    Behavior: Hard.
    Set the Bias Type as shown in the Details View.
    Bias Factor: 8.

## Slide 24: Local Sizing
Add Biased Edge Sizing
  In the Outline, right click on “Edge Sizing 2” and select Duplicate from the Context Menu.
  Under Details of “Edge Sizing 3”;
    Click the Geometry Selection Box and select the two edges as shown – do not hold down CTRL until you select the second edge.
    Set the Bias Type as shown in the Details View.

## Slide 25: Named Selections
Add Named Selections
  Right click and select Show All Bodies from the Context Menu.
  Right click on the single body part in the Outline and select Hide All Other Bodies.
  Snap to the +Z view using the Axis Triad.

## Slide 26: Named Selections
Add Named Selections
  Using the Face Selection Filter and the Box Select Tool select the faces of the impeller as shown.
  Right click and select Create Named Selection from the Context Menu.

## Slide 27: Named Selections
Add Named Selections
  In the Named Selection Dialog box enter the name impeller and click OK.

## Slide 28: Named Selections
Add Named Selections
  Select Single Select.
  Select the three faces surrounding the impeller and create a Named Selection “interface-inner”
  Right click, Show All Bodies.

## Slide 29: Named Selections
Add Named Selections
  Select the two faces forming the shaft and create a Named Selection “shaft”.

## Slide 30: Named Selections
Add Named Selections
  Select any one of the outer faces and select Extend to Limits.
  Create a Named Selection “tank”.

## Slide 31: Named Selections
Add Named Selections
  Hide the impeller body by right clicking it in the Outline and selecting Hide Body.
  Switch on the section plane and select all five faces forming the cavity as shown.
  Create a Named Selection “interface-outer”.
  Switch off the Section Plane.

## Slide 32: Named Selections
Add Named Selections
  Finally, create Named-Selections for the two fluid domains.
  Select the single body part from the Outline, right click and Create Named Selection “fluid-inner”.
  Select the five bodies from the multibody part, right click and Create Named Selection “fluid-outer”.
  Right click, Show All Bodies.

## Slide 33: Global Inflation
Setup Inflation
  Select the Mesh object in the Outline to display Details of “Mesh”.
  Under Inflation set;
    Use Automatic Inflation: All Faces in Chosen Named Selection.
    Named Selection: impeller.
  Under Statistics set;
  Mesh Metric: Orthogonal Quality.
  Generate Mesh.

## Slide 34: Final Mesh
Check and Inspect the Mesh
  Minimum Orthogonal Quality is acceptable.
  Snap to the +Z view using the Axis Triad.
  Create a new Section Plane horizontally as shown.

## Slide 35: Final Mesh
Check and Inspect the Mesh
  Use both Section Planes to inspect the mesh interior.

## Slide 36: Save the Project
  This completes the workshop.
  From the main menu select File  Close Meshing
    Workbench will save any application data.
  From the Workbench Project Page use the file menu and save the project as “AMWS5a.wbpj” to your working folder.

## Slide 37: Notes
  Rotating/moving parts can be solved using sliding meshes utilising non-conformal interfaces as demonstrated here or, for rotating parts, by an alternative method utilising rotating reference frames.
  The latter method does not need a non-conformal interface though it does still require the rotational zone to be contained within its own body. In this case the methods of geometry construction and meshing are the same with the exception that the rotating zone would be included in the multibody part along with all other bodies and a conformal mesh produced.
  Both methods have respective advantages. More information on solving such cases is covered in the solver training courses.