## Slide 1: Workshop 5c Applications - 2D Conical Combustion Chamber

## Slide 2: Introduction
Background
  This workshop will demonstrate the practical application of ANSYS Meshing to a 2d Conical Combustion Chamber Model.
Objectives
  Generating 2d Meshes
  2d Inflation
  Generating Mapped Meshes
  Parameterizing Mesh Controls

## Slide 3: Project Startup
Create the Project
  Start Workbench.
    Start  All Programs  ANSYS 14.5  Workbench 14.5
  If have access to DesignModeler, follow the instructions below.
    This workshop uses the geometry created in workshop 5c of the DesignModeler course. Open your saved project (DMWS5c) and drag and drop a Meshing component system onto the Geometry Cell (A2) as shown. If you did not complete this workshop, a copy is provided in the Meshing Workshops “Input-Files” folder.

## Slide 4: Project Startup
Create the Project
  If you do not have access to DesignModeler follow these instructions
  Drag and drop a Mesh component system into the Project Schematic .
  Right click on the Geometry cell (A2) and select Import Geometry  Browse.
  Locate the file “conical-surf.igs” in the Meshing Workshops Input Files folder and select it. The geometry cell will show a check mark indicating it is up to date.

## Slide 5: Analysis Type
Set Analysis Type
  Right click on the Geometry Cell in the Mesh System and select properties from the Context Menu.
  In the Properties Schematic set Analysis Type to 2D.

## Slide 6: Project Startup
Starting Meshing
  On the Mesh cell right click and select Edit
    Double clicking on the Mesh cell can also startup Meshing
  ANSYS Meshing will start up and load the geometry

## Slide 7: Units
Set Units
  From the main menu select Units and, if it is not already set, specify Metric (mm...).

## Slide 8: Preparation
Planning
  This geometry contains a 2d axisymmetric model representing a simple combustion chamber.
  Initially we will demonstrate simple 2d meshing methods on the model.
  The final mesh will use a mapped control to create a fully structured high quality mapped mesh over the entire surface using Local Edge Size Controls to define the level of mesh refinement.
  Local Mesh Controls will be parameterized to enable quick adjustment from the Workbench interface.
Gases In
Products of Combustion Out
2d Axisymmetric Section
3d Chamber Model

## Slide 9: Global Mesh Controls
Mesh
  In the Outline, select the Mesh object to display Details of “Mesh”.
  In Details of “Mesh”, set the following under Defaults;
    Physics Preference: CFD.
    Solver Preference: FLUENT.
  Under Sizing set Use Advanced Size Function: On: Curvature.
  Set Relevance Center to Fine.

## Slide 10: Named Selections
Add Named Selections
  Select the Edge Selection Filter
  Select the edge as shown (right).
  Right click and select Create Named Selection from the Context Menu.
  In the Named Selection Dialog Box type the name “inlet” as shown (right).
  Click OK.
  Use the same procedure to create a Named Selection for “outlet”.

## Slide 11: 2d Methods
Generate Mesh
  Generate the Mesh.
    With no methods or controls set the default automatic method generates a Quad Dominant Mesh.
    Note the majority of the mesh contains quad cells with just a few tri cells.

## Slide 12: 2d Methods with Inflation
Add Inflation
  In the Outline, right click on Mesh and select Insert  Inflation from the Context Menu.
  Select the Face Selection Filter.
  Select the Face and apply the selection in the Geometry Selection Box in the Details View.
  Activate the Boundary Selection Box.
  Select the ten edges as shown (all edges except the inlet and outlet) and apply the selection.

## Slide 13: 2d Methods with Inflation
Add Inflation (Continued)
  Check that the remaining details match those shown (right).
Add Method
  Select the Body Selection Filter.
  Select the Surface Body, right click and select Insert  Method from the Context Menu.

## Slide 14: 2d Methods with Inflation
Add Method (Continued)
  In the Details View set Method to Triangles (the Quad Dominant Option is the Automatic default).
  Generate the Mesh.
  Select Mesh in the Outline to redisplay the Mesh.
  The mesh contains tri cells within the surface.
    Inflation has generated quads on the boundary edges specified in the inflation control.

## Slide 15: 2d Methods (Uniform)
Add Method (Continued)
  In the Outline, select All Triangles Method.
  In the Details View set;
    Method to Multizone Quad/Tri.
    Surface Mesh Method to Uniform
    Free Face Mesh Type to All Quad
    Element Size to 2mm
    Suppress Inflation setting
  Generate the Mesh.
    Select Mesh to redisplay the mesh.
    A mesh containing 100% quad cells is generated using the size specified in the method details.

## Slide 16: Map Control
Add Map Control
  In the Outline, suppress both Multizone Quad/Tri Method and Inflation Controls by right clicking on them and selecting Suppress from the Context Menu.
  Select the Face Selection Filter.
  Select the face, right click and select Insert  Mapped Face Meshing from the Context Menu.

## Slide 17: Map Control
Add Map Control (Continued)
  In the Details View, activate the Specified Corners Selection Box.
  Select the two vertices (CTRL click to multiple select).
  Apply the selection.
  Generate the Mesh.

## Slide 18: Map Control
Add Map Control (Continued)
  Note the structure of the mapped mesh. The two vertices specified as Corners have two grid lines enabling the surface to be fully mapped.
    It is not always necessary to specify vertex types as in many cases vertices will be automatically specified. It is however recommended to become familiar with this procedure since vertices may need to be specified for more complex surfaces or if the surfaces are parameterized such that extensive changes may take place.
S
E
E
E
E
E
E
C
C

## Slide 19: Local Sizing
Add Edge Sizing
  Right click on Mesh in the Outline and select Clear Generated Data from the Context Menu.
    Answer Yes to the dialog box.
  Select the Edge Selection Filter.
  Select the two short edges (CTRL click to multiple select).
  Right click and select Insert  Sizing from the Context Menu.

## Slide 20: Local Sizing
Add Edge Sizing (Continued)
  In the Details View set;
    Type to Number of Divisions.
    Number of Divisions to 10.
    Behaviour to Hard.
  Parameterize the Number of Divisions by checking the box.
  Zoom in to preview the Edge Sizing.

## Slide 21: Local Sizing
Add Edge Sizing (Continued)
  Select the two edges shown (CTRL click to multiple select).
  Right click and select Insert  Sizing from the Context Menu.
  Populate the Details View as shown below and Parameterize the Number of Divisions as before.

## Slide 22: Local Sizing
Add Edge Sizing (Continued)
  Select the two edges shown (CTRL click to multiple select).
  Right click and select Insert  Sizing from the Context Menu.
  Populate the Details View as shown below and Parameterize the Number of Divisions as before.

## Slide 23: Local Sizing
Add Edge Sizing (Continued)
  Select the single edge shown.
  Right click and select Insert  Sizing from the Context Menu.
  Populate the Details View as shown below and Parameterize the Number of Divisions as before.

## Slide 24: Local Sizing
Add Edge Sizing (Continued)
  Select the two edges shown (CTRL click to multiple select).
  Right click and select Insert  Sizing from the Context Menu.
  Populate the Details View as shown below and Parameterize the Number of Divisions as before.

## Slide 25: Planning
Preparation
  We need to define edge sizing with an equal number of divisions for the two lines such that the sizing is biased as shown.
  The direction of Biasing depends upon the edge direction sense which can be viewed using the Edge Direction button in the Toolbar.
  In this case we can see that the edge directions are opposite – for this reason we’ll need to create individual edge sizing controls for each edge using opposite bias types.
  Switch off the Edge Direction Display.

## Slide 26: Local Sizing
Add Edge Sizing (Continued)
  Select the single edge shown.
  Right click and select Insert  Sizing from the Context Menu.
  Populate the Details View as shown below and Parameterize the Number of Divisions as before.
  Note the Bias Type & Factor Settings.

## Slide 27: Local Sizing
Add Edge Sizing (Continued)
  Select the single edge shown.
  Right click and select Insert  Sizing from the Context Menu.
  Populate the Details View as shown below and Parameterize the Number of Divisions as before.
  Note the Bias Type & Factor Settings.

## Slide 28: Final Mesh
Generate the Final Mesh
  Generate Mesh.
  In the outline, select Mesh.
  In the Details View, under Statistics, set Mesh Metric to Orthogonal Quality.
  Note the high quality of the mapped mesh.

## Slide 29: Planning
Preparation
  Although we have a good quality fully mapped mesh if we wanted to refine the mesh we would need to change all eight edge sizing details.
  In some cases we may need to do this many times to accommodate for initial mesh independency studies, geometric changes or changes to the physics or boundary conditions in the solver.
  To make this process easier we can create a function inside workbench using the parameterised edge sizings.

## Slide 30: Parameterization
Parameterize Sizing
  Switch to the Workbench Project Page.
  Double click on Parameter Set.
  In the Outline of All Parameters, double click in the box under “Edge Sizing 7…” and type in the name of a new parameter “Mesh Factor”
  In the box to the right (“New Expression”) double click and enter 1.
  *Note, if you started the workshop using the imported .igs file the first Geometry Parameter will not exist. Your parameter numbering will therefore be P1 to P7.

## Slide 31: Parameterization
Parameterize Sizing (Continued)
  Click in the first edge sizing parameter to select it.
  In the box “Properties of Outline..” double click in the Value box to the right of “Expression” and type in 10*P9.
    This converts parameter P2 to a function of the original number of divisions and the new parameter we created – P9 “Mesh Factor”.

## Slide 32: Parameterization
Parameterize Sizing (Continued)
  Do the Same for the remaining edge sizing parameters using the following expressions for each.
    P3 = 10*P9
    P4 = 15*P9
    P5 = 20*P9
    P6 = 7*P9
    P7 = 30*P9
    P8 = 30*P9
  In the Table of Design Points you can now change the “Mesh Factor” parameter (P9) to drive all eight edge sizing parameters.
  Set it to 2 and press enter. The other parameters will be evaluated.

## Slide 33: Parameterization
Parameterize Sizing (Continued)
  Click Update Project.
    This will send the newly evaluated values for the parameterized edge sizing back to the meshing application and regenerate the mesh.
  Switch back to the Meshing Application to view the regenerated mesh with the new sizes.
  You can now create a number of design points each using a gradually refined mesh controlled by a single Parameter*.
  *Care should be taken to ensure that expressions return useable values. In this case we have parameterised edge sizing ‘interval numbers’ therefore our expressions must return whole integers. If the edge sizings required ‘size’ then real numbers would also be acceptable.

## Slide 34: Save the Project
  This completes the workshop.
  From the main menu select File  Close Meshing
    Workbench will save any application data.
  From the Workbench Project Page use the file menu and save the project as “AMWS5c.wbpj” to your working folder.