## Slide 1: Workshop 5d Applications – Assembly Meshing

## Slide 2: Introduction
Background
  This workshop will demonstrate the application of Assembly Meshing to a CAD import assembly of parts.
Objectives
  Starting ANSYS Meshing
  Activating Assembly Meshing
  Creating a Material Point
  Creating a Virtual Body
  Inflation
  Defining a Fluid Surface
  Generating the Fluid Mesh

## Slide 3: Project Startup
Create the Project
  Start Workbench.
    Start  All Programs  ANSYS 14.5  Workbench 14.5
  Drag and drop a Mesh component system into the Project Schematic .
  Right click on the Geometry cell (A2) and select Import Geometry  Browse.
  Locate the file “mixer-t.stp” in the Meshing Workshops Input Files folder and select it. The geometry cell will show a check mark indicating it is up to date.
  Double click on the Mesh Cell (A3) to start Meshing.

## Slide 4: Units
Set Units:
  In the Units menu set Metric (mm, kg, N, s, mV, Ma)

## Slide 5: Preparation
Planning
  This assembly consists of four solid bodies (representing the solid pipe wall and flanges) and three surface bodies (caps) that cap all the pipe entrances/exits.
    Note that the bodies do not form a single part (the bodies are not connected). There is also no defined fluid body.
  Assembly Meshing can generate fluid meshes on this type of CAD import by providing a material point (coordinates) within the volume occupied by the fluid. The specification of a material point is used to create a ‘Virtual Body’ representing the fluid region.
  A conformal mesh can also be generated in and across the solid parts.

## Slide 6: Global Mesh Controls
Set Defaults and Activate Assembly Meshing
  In the Outline, select the Mesh object to display Details of “Mesh”.
  In Details of “Mesh”, set the following under Defaults;
    Physics Preference: CFD.
    Solver Preference: Fluent.
  Under Assembly Meshing set;
    Method: CutCell.

## Slide 7: Global Mesh Controls
Set Defaults and Activate Assembly Meshing (Continued)
  Under Sizing check that Use Advanced Size Function is set to On: Curvature.
    Note that when using Assembly Meshing the Advanced Size Function cannot be deactivated (must be set to one of four options).

## Slide 8: Material Point
Create a Coordinate System
  In the Outline, right click on Coordinate Systems and select Insert  Coordinate System from the Context Menu.
  In the Details View, activate the Geometry Selection Box (click in the box to the right of Geometry – Apply/Cancel buttons will appear).
  Select the Body Selection Filter.

## Slide 9: Material Point
Create a Coordinate System (Continued)
  Select the central solid body as shown (right) and apply the selection in the Details View.
    A new coordinate system has been created using the centroid of the selected body as origin coordinates.
    The Coordinate System is listed in the Outline, the origin coordinates in the Details View and displayed in the Graphics window.

## Slide 10: Virtual Body
Create a Virtual Body
  In the Outline, right click on Geometry and select Insert  Virtual Body from the Context Menu.
  In the Details View, click in the Material Point box and select the new coordinate system from the drop down menu as shown.

## Slide 11: Global Mesh Controls
Mesh
  In the Outline, select the Mesh object to display Details of “Mesh”.
  In Details of “Mesh”, under Assembly Meshing a new option has appeared (Keep Solid Mesh).
    Set Keep Solid Mesh to Yes.
      This option appears in response to the presence of a Virtual Body representing the flow region. In such cases it is desirable to be able to choose whether or not to generate a mesh on both fluid and solid regions.
      Imported bodies can be defined as fluid/solid. In the Outline click on any of the bodies and note the Material assignment in the Details View.

## Slide 12: Generate Mesh
Generate Initial Mesh
  Select the Mesh object in the Outline.
  Generate the mesh.
    A Number of Messages will be printed in the Message Box prompting the user to check the mesh for geometric accuracy.
  Note the feature capture failure (right).
  Poor feature capture can be fixed in a number of ways. The simplest approach is to try refining the mesh in these regions. In this case, since the mesh is quite coarse on all the pipe faces, we will decrease the Global Curvature Normal Angle. This will create smaller cells on all curved faces including the problematic area.

## Slide 13: Generate Mesh
Adjust Sizing and Generate Mesh
  In the Details View, under Sizing change Curvature Normal Angle to 10.
  Generate the mesh.
  The new, more refined, mesh has eliminated the previous feature capture problem.
    Note that warning messages may still appear even if the mesh is acceptable in terms of geometric feature capture.

## Slide 14: Section Plane
View Mesh Interior
  Right click in the graphics window and select View  Front (corresponds to -Z).
  Select the Section Plane Tool.
  Create a Section Plane by clicking, dragging and releasing as shown vertically down through the mesh.

## Slide 15: Section Plane
View Mesh Interior (Continued)
  Set the view to isometric using the Iso Ball.
  Zoom in using the Box Zoom tool as shown.
  Note that the mesh between the parts is fully conformal.
  In the Outline, select the Mesh object to display Details of “Mesh” and, under Statistics, set Mesh Metric to Orthogonal Quality.
  Orthogonal Quality is acceptable (above 0.05).

## Slide 16: Mesh Metrics Graph
View Mesh Interior (Continued)
  Note that the Mesh Metrics Graph indicates that the mesh contains different cell types.
    If the graph is not visible click the Metric Graph button.
  You can see from the graph bars that, for each range of quality, hexahedral cells are the most prevalent (dark blue) followed by wedge cells (green). Other cell types form only a small part of the mesh.
  Switch the Metric Graph off using the Metric Graph button.

## Slide 17: Inflation
Add Automatic Inflation
  In the Details View, under Inflation set Use Automatic Inflation to Program Controlled leaving all other settings to the defaults as shown.
    In Assembly Meshing;
      When inflation is required on Virtual Bodies, Automatic Program Controlled Inflation must be used.
      Automatic Program Controlled Inflation will create inflation in fluid bodies (Virtual Bodies are fluid by default). Solid bodies will contain no inflation.

## Slide 18: Named Selections
Add Named Selections
  Click the Zoom to Fit button to restore the view.
  Select Geometry in the Outline.
  Select the Face Selection Filter
  Select the face as shown.
  Right click and select Create Named Selection from the Context Menu as shown

## Slide 19: Named Selections
Add Named Selections (Continued)
  In the Named Selection Dialog Box type the name “outlet” as shown (below).
  Click OK.
  Use the same procedure to create two more Named Selections (inlet-1 & inlet-2) for the faces shown below.
Inlet-1
Inlet-2

## Slide 20: Inflated Mesh
Generate Inflation Mesh
  Generate the mesh.
    In Assembly Meshing Inflation is a post volume mesh procedure (the volume mesh will not be regenerated).
  Select Mesh in the Outline to redisplay the new inflated mesh.
  The Program Controlled Inflation has inflated into the fluid region (Named Selections have been excluded).
    Additional messages warn that inflation will not be carried out on sheet bodies or on defeatured geometry.
  Check the Statistics in the Details View and confirm that the Orthogonal Quality is still above 0.05.

## Slide 21: Preparation
Planning
  In many cases we are only interested in generating a mesh for the fluid region. We can use the ‘Keep Solid Mesh’ option under Assembly Meshing in the Details View to discard the solid mesh if required.
  However, this option will still initially generate the solid & fluid body meshes. The solid mesh will simply be discarded after this process. For small cases this is not a problem but for larger cases this can become very inefficient in terms of time.
  We can avoid this by defining which faces are ‘wetted’ by the fluid before we generate the mesh with the ‘Keep Solid Mesh’ option set to No.
Wetted Surfaces

## Slide 22: Fluid (Wetted) Surfaces
Insert Fluid Surface
  In the Outline clear the existing mesh by right clicking on Mesh and selecting Clear Generated Data from the Context Menu.
  Expand Geometry then, under Geometry, expand Virtual Body Group.
  Right click on Virtual Body and select Insert  Fluid Surface from the Context Menu.

## Slide 23: Fluid (Wetted) Surfaces
Insert Fluid Surface (Continued)
  In the Details View activate the Faces To Group selection box.
  Select the eight faces as shown and apply the selection (CTRL click to multiple select).
    The selected faces representing the Fluid Surfaces will by colored blue/red.

## Slide 24: Assembly Mesh Options
Solid Mesh Option
  In the Outline, select the Mesh object to display Details of “Mesh”.
  Under Assembly Meshing, set Keep Solid Mesh to No.
  Generate the Mesh.

## Slide 25: Final Fluid Mesh
Generate Mesh
  In the Outline, select the Mesh object to display Details of “Mesh”.
  Under Assembly Meshing, set Keep Solid Mesh to No.
  Generate the Mesh.
  When the mesh is generated switch off the Section Plane and view the final fluid mesh.

## Slide 26: Final Fluid Mesh
View Final Fluid Mesh
  In the Details View, under Statistics, confirm that the final Orthogonal Quality is acceptable (above 0.05).

## Slide 27: Save the Project
  This completes the workshop.
  From the main menu select File  Close Meshing
    Workbench will save any application data.
  From the Workbench Project Page use the file menu and save the project as “AMWS5d.wbpj” to your working folder.